Observing Jovian DAM Emissions with a SDR Telescope

---
SDR what makes it interesting?
- Availability of cheap receivers such as the DVB-T HDTV tuners and transceivers such as the HackRF has lead to explosion in popularity of SDR and allows amateur enthusiasts access to the airwaves
- SDR allows the manipulation of radio communication signals from within software. Eg: Can listen to several different frequencies at once
- I've been fascinated by Astronomy and Space in general for as long as I can remember. Jupiter is an interesting target for observation either visually or through a radio telescope, and after reading about the DAM emissions and strange interactions with its satellite Io I've been wanting to hear them for myself!

---
DAM Emissions
Jupiter emits radio waves in the decametric (DAM) range (10 – 100 m wavelengths or 4 – 40MHz frequencies)

---
Aims
- Build an antenna which can pick up DAM Emissions
- Develop SDR Filter for interference emissions from natural and human sources
- Develop SDR solution to identify interesting Jovian DAM emissions
- Design automated listening station, and aggregation, DSP backend for multiple listening sites

---
DAM Emissions, where do they come from?

---
How can the DAM emissions be Observed?

---
How can SDR be leveraged to process signals observed?

---
Hypothesis
- What IOT technologies would lend themselves to develop a scalable self sufficient listening platform for radio communication
- Is it possible to develop an Opensource SDR data processing solution to detect interesting DAM events such as S-Bursts, L-Bursts or N-Bursts
- Can an Opensource SDR solution in be developed to process the observation data to flag or filter natural or human created interference

---
Methodology
- Build antenna: Dual Dipole antenna as described in the NASA Radio Jove project
- Perform site survey with a spectrum analyser to determine if the Antenna is suitable to capture DAM emissions either from Jupiter or the Sun
- Develop an automated system to Collect data from the antennae
- Develop a SDR solution to perform digital signal processing on the captured data

---
Project Plan

---
Conclusions
- While it is still early in the process, there are a number of limitations of the study already identified
- Solution geared towards a telescope listening site with a Latitude of 53.3 Degrees N
- An embedded computer such as the Raspberry Pi, Beaglebone Black or Intel Gallileo is unlikely to be powerful enough to perform serious signal processing on site.
- Might require more powerful system such as an Intel Atom or i3/i5/i7 system due to intensive USB transfer rates at high bandwidths with the transceiver